## Slide 1
P2 Electricity
Current is the flow of charge
Wire – electrons
Solutions - ions
Resistance reduces the current
High resistance = low current
Potential difference is the driving force that pushes the charge round
Increase voltage = high current
Units
Current - A
Potential difference - V
Resistance - Ω
Charge - C
Time - s
Length - m
Take care – convert units!!!
1A = 1000mA
1V = 1000V
Uses these equations!!!

## Slide 2
A resistor reduces the current
All resistor symbols have a box
  Fixed resistor
  Fuse
  LDR
  Thermistor
  Variable resistor
A Diode only allows the current to flow in one direction – look for the “play” symbol
Diode
LED
A fuse contains a metal wire – this melts when the current is too high
Ammeter is placed in series
Voltmeter is placed in parallel

## Slide 3
A longer length wire
Has more metal ions
Therefore more collisions occur between the electrons and metal ions
More collisions = more resistance which reduces the current
Effects of length of wire and resistance
A shorter length wire
Less collisions results in less resistance
Current increases
A high current causes the wire to get hot and could go on fire!!!
Keep one crocodile clip at 0m and move the other at different distances
Measure the potential difference and current for each length and calculate the resistance
Graph:
length of wire against resistance
Directly proportional must go through (0,0)

## Slide 4
A – wire cold, few collisions between ions and electrons
Little resistance so high current
Directly proportional
A
B
Non – ohmic conductor
e.g. fixed resistor
Temperature remains constant
B – wire hot, ions vibrating more, so more electrons collide with ions
* More resistance less current
A
B
Non – ohmic conductor
A – if the potential difference is in the opposite direction, there is a high resistance and current does not flow
B – if the potential difference is in the correct direction, then current flows through the diode in one direction
Temperature / light
Thermistor and LDR work in the same way
thermistor’s resistance changes with temperature
LDR changes resistance with light
High temperature / light = low resistance = high current
Low temperature / light = high resistance = low current

## Slide 5
Series Circuit
Potential difference shared
Vtotal = V1+V2 +…
Current same
I1 = I2=…
In series add up the resistance Rtotal = R1 + R2
example
V=IR
Resistance bulb 1 = 3/2
= 1.5Ω
Resistance bulb 2 = 3/2
= 1.5Ω
Total resistance = 1.5+1.5
=3Ω
1
2
Parallel Circuit
Take care – things are different for a parallel circuit
Voltage the same across all components V1=V2=…
Current is shared between branches
A3 (total) = A2+A1
* Total resistance is less than the resistance of the smallest resistor
More than one loop
series
parallel
More resistors = increase resistance
More resistors = decrease resistance

## Slide 6
Direct current – current flows in one direction
Current is either always positive or negative
Alternating current, changes direction 50 times every second.
Frequency 50Hz
230V
Current alternates between positive and negative
Electricity in the home
Earth – safety
0V
Live – 230V
Neutral –0V
Fuse – safety, metal wire melts to break the circuit – high current
Double insulated provides an extra layer of insulation to prevent electric shock

## Slide 7
Power
Energy is transferred to an appliance to make it work
The more energy transferred in a given time, the higher the power.
E=Pt
E energy (J)
P power (W)
t time (s)
Be able to convert units
1kW = 1000W
Transferring energy to an appliance
The power of an appliance can also be calculated
P=VI
P=I2R
Be able to use all equations and convert

## Slide 8
National Grid
National grid
Giant system of cables and transformers that covers the UK
Transfers electrical energy from power stations to consumers
Power station generates electricity
Energy is lost through powerlines
More energy lost if current is high!!!
Step up transformer
Increases potential difference
To keep power the same P=VI
Current is reduced
Low current reduces heat loss as electrical energy is transferred along power lines
Step down transformer
Decreases potential difference
To keep power the same P=VI
Current is increased
Voltage is decreased for safety